## Slide 1: HOW TO BULID NETWORK
By
SHARATH BALAN

## Slide 2: Network devices
Modem
Rj-45
nic (Network Interface Card)
Ethernet card
Hub
Router

## Slide 3
MODEM

## Slide 5: Setting up a home network – components and structure
Router or Wireless router – Connects the network to the Internet.
Wireless Access Point – Used to Connect Wi-Fi equipped devices to the network.
Ethernet HUB or Switch -Used to Connect Ethernet equipped devices.
Cable cat 5, cat5e or cat 6 with RJ45 connectors.
Telephone Cable with RJ 10 connectors.
Broadband Filters.

## Slide 7: SETTING UP ACOMPUTER NETWORK
The network functioning is based on Client-Server architecture which requires effective and efficient network design. It defines how clients are connected to server machine on a network. The most important rule or methodology for network (LAN) design is the 80:20 rule

## Slide 8: 80:20 THUMB RULE
This thumb rule states that in a well-organized and designed network, 80 percent of the traffic on a given network segment is local (i.e., destined for a destination system in the same workgroup), and not more than 20 per cent of the network traffic should move across a backbone. The backbone in a network which violates this 80:20 rule leads to network congestion and traffic jams.

## Slide 9: Problem 1.0
An educational society (say XYZ Educational Society), with its head office in Chennai (Tamil Nadu) and schools in various parts of the globe, is setting up a new senior secondary school, ‘SF School’, in Haryana. The ‘SF School’ will have 3 computer labs with 30 computers in each lab, one Accounts office with three computers, one Administrative block with five computers, and a Principal’s office with one computer

## Slide 10
Let us see how a computer network can be set up in the school. First of all, we can draw a rough sketch of the school with computers at various locations as follows:
1. Independent LANs can be set up in each of the following buildings: Computer Lab1, Computer Lab2, Computer Lab3, Administrative Block and Accounts Office.
2. These LANs can be set up in STAR topology using UTP cable (economical, reliable and easily available).
3. For this, one switch (with suitable number of ports) will be required in each of these buildings. More than one switch can be used in computer labs if a switch with more than 30 ports is not available.
4. Two internet connections (broadband for high speed) can be procured in Administrative Office. Two connections should be procured from two different ISPs so that: (a) Internet connection in Administrative office can be kept separate from the other Computer labs where students may do a lot of experimentation

## Slide 11
(b) If one internet connection is not working, the other can be used in case of urgent requirements
5. These buildings can then be connected as follows
6. This interconnection will ensure that each
building is directly connected to Administrative
block.
7. This way, internet connection will be available in each building irrespective of the status of the other building.
8. Server (if any) of the school may be placed in the Administrative block so that it remains safe (physically) and a firewall can be set up so that the whole network remains safe from any kind of virus or intrusion attacks.
There is no need to put in any extra efforts or expenses to link the school to its head office. This can be taken care of using the internet connections

## Slide 12: THANK YOU